Date: September 27, 2016

Dear Valued Customer:

IMPORTANT  SAFETY  RECALL

Regarding your:  2014-2015 Tuono V4 1000, 2016 Tuono V4 1100, 2015 Caponord 1200 or 2016

Caponord Rally

THIS NOTICE APPLIES TO YOUR VEHICLE    VIN: __________________________________

This notice is sent to you in accordance with the requirements of the National Traffic and Motor Vehicle Safety Act. The NHTSA identification number of this recall is 16V-691

# REASON FOR THIS RECALL

Aprilia USA has decided that a defect, which relates to motor vehicle safety, exists in a specific range of Aprilia motorcycles noted below:

      - Select  MY 2014-2015 Tuono V4 1000

      - Select  MY 2016 Tuono V4  1100

      - Select  MY 2015 Caponord 1200

      - Select  MY 2016 Caponord Rally

In the affected range, Aprilia USA has identified front brake master cylinders which do not meet our exacting standards. These non-conformant front master cylinders may have a defective hydraulic circuit, which in certain conditions, may result in longer than normal braking distances.  According to vehicle registration records, you are the owner of a vehicle that falls within this affected VIN range.

# WHAT WE WILL DO

To address this situation, Aprilia USA will conduct a recall of 2014-2015 Tuono V4 1000, 2016 Tuono V4 1100, 2015 Caponord 1200 and 2016 Caponord Rally models within the affected VIN range. Aprilia USA, through the qualified dealer network, will replace the front master cylinder pushrod and boot assembly.  This repair campaign will eliminate any potential safety risk.

The work required by this recall may be completed by your qualified Aprilia dealer at no charge to you for the required parts and labor. The work time for the repair is approximately 25 minutes.

# WHAT YOU SHOULD DO

With the receipt of this letter, please contact your authorized Aprilia dealership as soon as possible to schedule an appointment to have the recall completed. Instructions for this recall have been sent to your dealer and the parts are available. Your dealer is best equipped to obtain parts and provide service to ensure that your vehicle is corrected as promptly as possible. Please ensure that these instructions are followed by anyone that uses your vehicle.

If you take your vehicle to your dealer on the agreed service date and they do not remedy this condition on that date or within three (3) days, we recommend you contact our Customer Care helpline at: 212-380-4433.

After contacting your dealer and the above number, if you are still not able to have the safety defect remedied without charge and within a reasonable time, you may wish to write to: The Administrator, National Highway Traffic Safety Administration, 1200 New Jersey Ave SE, Washington, DC 20590, or call the toll-free Vehicle Safety Hotline at 1-888-327-4236 (TTY: 1-800-424-9153); or go to http://www.safercar.gov.

Our Customer Care helpline (212-380-4433) is available to provide you with further information and any support you may need. Should the vehicle not be in your possession or available to you, please provide the name and address of the purchaser by contacting our Customer Care department or by filling out the form on the following page. This form can be faxed to 212-380-4459.

If you previously had the work required of this recall completed at your own expense, please refer to the attached letter (Tread Act Customer Reimbursement Plan) describing the criteria and procedure to request reimbursement.

Federal law requires any lessor who receives a notification of a determination of a safety-related defect or noncompliance pertaining to any leased motor vehicle shall send the notice to the lessee within 10 days.

We are sorry to cause this inconvenience; however, we have taken this action in the interest of your safety and continued satisfaction with our products. Thank you for your prompt attention to this important matter.

Very truly yours,

Aprilia USA

Piaggio Group Americas

Tuono V4 1000/1100 & Caponord 1200/Rally

## VIN # (Full 17 digits):   _  _  _  _  _  _  _  _  _  _  _  _  _  _  _  _  _

New Owner Details (if not in your possession)

First Name: _______________________ Last Name: ________________________________

Street Address: _______________________________________________________________

City: _____________________________    State: __________________ Zip: _____________

Date of transfer: _____________________

Vehicle not available for the following reasons:  Scrapped: ______ 	Stolen: ______

Vehicle not available for other reasons: (Please specify)

__________________________________________________________________________________

__________________________________________________________________________________

__________________________________________________________________________________

Print Name: ______________________________________

Signature: ________________________________________Date: _____________________________

TREAD ACT CUSTOMER REIMBURSEMENT PLAN

Customer Reimbursement for Safety Related Recall Repairs

Effective with Safety related recalls initiated as of January 15, 2003

Aprilia USA is initiating a safety related recall for a select range of 2014-2015 Tuono V4 1000, 2016 Tuono V4 1100, 2015 Caponord 1200 and 2016 Caponord Rally models that includes your VIN number. If you have previously paid to have the repair or update as described in the recall documentation completed, you are entitled to be reimbursed for that expense.

You are encouraged to request reimbursement from your respective Aprilia dealer.  Alternatively, you may submit the request for reimbursement to the following address:

Customer Care

Aprilia USA

257 Park Avenue South, 4th Floor

New York, NY 10010

In every case:

- Repair expenses pertaining to the subject of the safety recall are reimbursable, not consequential expenses such as towing, rental, accommodations, damage repairs, etc.

- Expenses from repair facilities outside of the Aprilia USA authorized dealer network will be considered; however, the repair procedure must meet Aprilia USA’s standards.

- When reimbursing for parts, the Manufacturers Suggested Retail Price (MSRP) will be considered as the guideline for reasonable charges.

- Expenses for repairs performed more than 10 days after the date of the last customer notification letter sent by Aprilia USA are not eligible for reimbursement.

- Taxes and hazardous waste disposal, where previously paid, are eligible for reimbursement.

The authorized  Aprilia dealer will request a copy of the customer notification letter, as well as a copy of the owner’s previously paid invoice, and then inspect the vehicle (if still in the possession of the invoice holder) to determine the scope and quality of the previous repair.  Claims will be processed within 60 days of receipt.